## Slide 1
Team name: G3
Member: Daniel Odido, Rohith Shivashankar, Kerim Hadžić, Arno Barnard
Space based CO2 concentration monitoring

## Slide 2: Table of Contents
Mission Statement
System Design
Management
Demonstration
4.1 Experimental Setup: Planned vs Performed
4.2 Experimental Results
  Physical – Parachute
  Physical – CO2 GS Mode
  Physical – LEDs, Sound
  Operational – Satellite Bus Verification
  Operational – CO2 Sensors
  Operational – LEDs, Sound
  Operational – Python GS User Interface
  Functional – CO2 Software: Node + GS
  Functional – Parachute release with dummy weight
  Functional
  End to End Testing – CO2 Sensor
  End to End Testing – LEDs for Landing
  End to End Testing - System
4.3 Summary of Success Evaluation
Conclusion

## Slide 3
1.1 User Needs / Background
The major threat from increased CO2 is the greenhouse effect. As a greenhouse gas, excessive CO2 creates a cover that traps the sun's heat energy in the atmospheric bubble, warming the planet and the oceans.
One way to measure the CO2 in Space is including air quality sensor to Satellite .
The main objective of the mission is to Monitor the carbon dioxide in the space through satellite to understand climate change at different time, altitudes and compare the carbon dioxide content with ground station.
Mission System Design > 1. Mission Statement

## Slide 4
1.2 Sketch / Mission Statement
Mission System Design > 1. Mission Statement
Clarify objectives
  To set up a satellite system to monitor atmospheric concentration of carbon dioxide
  By sensing the concentration of carbon dioxide by sensors installed on the computer
  Using HEPTA-Sat with carbon dioxide sensor supported by a ground node
Mission Goals
  [MG1] Establish successful measurement of CO2 concentration at specified altitude
  [MG2] Establish successful measurement of CO2 concentration at ground node
  [MG3] Relay the measured values of CO2 concentration to the Ground Station

## Slide 5
1.2 Sketch / Mission Statement
Mission System Design > 1. Mission Statement

## Slide 6
1.3 Success Criteria
Mission System Design > 1. Mission Statement
Success Level | Goal No. | Mission Success Criteria | Verification Method
Minimum Success | 1 | Establish the communication between Stellite and GS | Switch on the satellite and HK Data Received
 | 2 | Get the CO2 data from Satellite | CO2 data from Satellite is Received Successfully
 | 3 |  | 
Full Success | 4 | Establish the communication between Stellite and GS | Switch on the satellite and House Keeping Data Received
 | 5 | Get the CO2 data from Satellite at the specified interval of time to GS | CO2 data from Satellite is Received Successfully
 | 6 | Detect landing condition | LED and Sound data received
Advanced Success | 7 | Establish the communication between Stellite and different GS | Switch on the satellite and House Keeping Data Received
 | 8 | Get the CO2 data from Satellite at the specified interval of time from Different GS and Compare the results | CO2 data from Satellite is Received to all the GS station Successfully
 | 9 | Detect landing condition and measure the force of impact of the ground (through acceleration) | LED and sound data is received

## Slide 7
2.1 Use Case Diagram
Mission System Design > 2. System Design

## Slide 8
2.2 Use Case Scenario Diagram
Mission System Design > 2. System Design

## Slide 9
2.3 State Machine Diagram
Mission System Design > 2. System Design

## Slide 10
2.4 Function Decomposition Diagram
Mission System Design > 2. System Design

## Slide 11
2.5 Sequence Diagram
Mission System Design > 2. System Design

## Slide 12
2.5 Sequence Diagram
Mission System Design > 2. System Design

## Slide 13
2.6 System Diagram
Mission System Design > 2. System Design

## Slide 14
2.7 Component Requirement - HeptaSat +
Mission System Design > 2. System Design
Component | MHZ19C
Target gas | CO2
Voltage | 5 V
Component | Model parachute
Dimension | 0.02x0.02x5 inches
Material | Nylon
Component | UGCM0903EPD
Rated voltage | 3.0 V
Minimum sound | 85 db
Component | C513A LED 5mm
Current | 10mA
Beam width | 60°

## Slide 15
3.1 Cost Management
Mission System Design > 3. Management
No. | Components | Model Number & URL | How to get | Qty | Unit Price | Total
1 | Carbon dioxide sensor | MH Z19C | Akizuki | 2 | 2,480 | 4,960
2 | MBED Processor LPC1768 |  | Available | 1 |  | 
3 | Sound beacon | UGCM0903EPD | Akizuki | 1 | 50 | 50
4 | Parachute | Estes Rockets | Self-made | 1 | 3000 | 3,000
5 | Light led’s |  | Akizuki | 5 | 20 | 100
6 | Hepta-sat |  | Available | 1 |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
 | Sub Total |  |  |  |  | 8150
 | Tax (10%) |  |  |  |  | 815
 | Grand Total (JPY) |  |  |  |  | 8965

## Slide 16
3.2 Schedule Management
Mission System Design > 3. Management
Action Item | Person in charge | Day 1 |  |  |  | Day 2 |  |  | 
 |  | 9 | 12 | 15 | 18 | 9 | 12 | 15 | 18
Build/Interface all the elements on to the board |  |  |  |  |  |  |  |  | 
Satellite Software Design and interfacing |  |  |  |  |  |  |  |  | 
Ground Station Interface and Software Design |  |  |  |  |  |  |  |  | 
Python coding and analysis |  |  |  |  |  |  |  |  | 
Testing a) Communication between Satellite to GS b) Sensor Data analysis |  |  |  |  |  |  |  |  | 
Measurements and Analysis |  |  |  |  |  |  |  |  | 

## Slide 17
3.3 Risk Management
Mission System Design > 3. Management
Degree of impact
Low
Mid
High
Low
Mid
High
Probability
- Satellite does not switch on after launch
- Communication uplink not working
- Failure due to integration
- Battery does not charge
- Satellite GPS measurement not working
- Satellite Camera not working
- Solar panel damage
- (Parachute damage)
Ground station not working
- CO2 sensor not working
-HResources

## Slide 18
3.3 Risk Management
Mission System Design > 3. Management
Risk | Countermeasures
Satellite does not switch on after launch | Test release mechanism thoroughly to have lowest possible risk - also test release in cold vacuum to check for possible cold welding of release switch
Communication uplink not working | Test communication over long enough distance to verify all connections with antennas integrated
Battery does not charge | Integrate battery level within software to monitor chagring and optimize usage. Test battery charging and solar panel interface thoroughly.
CO2 sensor not working | Do proper ground testing. There should be no jamming for CO2 sensor, protect from dirt by working in clean room only.
Satellite GPS measurement not working | Thoroughly test on ground to verify functionality. Test with GPS simulator to verify functioning at high velocities/altitudes.
Satellite Camera not working | Thoroughly test on ground to verify connections, lens integrity due to vibrations
Ground station not working | Test thoroughly and have spare parts available for repairs.

## Slide 19: …table of contents
Mission Statement
System Design
Management
Demonstration
4.1 Experimental Setup: Planned vs Performed
4.2 Experimental Results
  Physical – Parachute
  Physical – CO2 GS Mode
  Physical – LEDs, Sound
  Operational – Satellite Bus Verification
  Operational – CO2 Sensors
  Operational – LEDs, Sound
  Operational – Python GS User Interface
  Functional – CO2 Software: Node + GS
  Functional – Parachute release with dummy weight
  Functional
  End to End Testing – CO2 Sensor
  End to End Testing – LEDs for Landing
  End to End Testing - System
4.3 Summary of Success Evaluation
Conclusion

## Slide 20
4.1 Experimental Set-up - Planning vs Performed
Exp 1 - Hepta-Sat with ground station setup as per textbook instructions
    Battery charging and power supply will be verified - Completed
    Communication will be verified by transmitting commands - Completed
    9-Axis functionality will be verified - Completed
    GPS will be verified - Completed
Exp 2 - With added CO2 sensor system functionality is tested
    First with both satellite and GS next to each other, should have the same CO2 measurements from both - Completed for GS node only
    Next test with satellite removed from ground station, to verify CO2 measurement scheduling, sampling and data transfer - Data transfer of dummy data only, no scheduling
    Move satellite to other CO2 environment - enclosed, or controlled, or at different altitude. Check that CO2 levels measured by satellite change - Used GS node as proxy for satellite, tested indoors, outdoors, different altitudes (floor indoors), breath test
Exp 3 - For secondary mission(s)
    Attach parachute and test if images give enough detail to be useful - Parachute not attached due to risk, parachute reliability tests completed
    Simulate satellite movement and then put down on still surface, check if recovery support of LEDs and Sound are activated - Completed
Mission System Design > 4. Demonstration

## Slide 21
4.2 Experimental Result - Physical - Parachute
Mission System Design > 4. Demonstration
Diameter :90 Cm
Threads Used: 8
Weight: 100 ML water bottle

## Slide 22
4.2 Experimental Result - Physical - CO2 GS node
Mission System Design > 4. Demonstration
CO2 sensor and MBED micro integrated

## Slide 23
4.2 Experimental Result - Physical - LEDs, Sound
Mission System Design > 4. Demonstration
CO2 sensor
LED wires and series resistors

## Slide 24
4.2 Experimental Result - Operational (1/4) - Satellite Bus Verification
Mission System Design > 4. Demonstration
Charging, power, 9-axis, GPS, Camera, Communication

## Slide 25
4.2 Experimental Result - Operational (2/4) - CO2 sensors
Mission System Design > 4. Demonstration
  GS setup - serial comms and protocol
    Software was developed
    Tested independently of satellite
    Completely functional
  Integration in satellite - serial comms and protocol
    Software developed
    Tested with satellite bus software
      Protocol fully functional
      CO2 interface non-functional

## Slide 26
4.2 Experimental Result - Operational (3/4) - LEDs and Sound
Mission System Design > 4. Demonstration
LED integration in satellite - Software control
  Landing detection software completely functional
Sound sensor integration in satellite - Software control
  Sound Sensor not completed

## Slide 27
4.2 Experimental Result - Operational (4/4) - Python GS GUI
Mission System Design > 4. Demonstration
Updated Python code snippets

## Slide 28
4.2 Experimental Result - Operational (4/4) - Python GS GUI
Mission System Design > 4. Demonstration
Expanded Python User interface
  GS GUI Development and testing
    added functionality for second comms channel to CO2 sensor
    partial success, UART comms for second channel not displayed

## Slide 29
4.2 Experimental Result - Functional (1/4) -
CO2 Software: Node + GS
Mission System Design > 4. Demonstration
Descriptions + pictures with annotations
  CO2 to GS comms/ to sat comms
    Power on test
    CO2 sending (using scope)
    CO2 response (using scope)
    Sat comms SW approach - limited functionality

## Slide 30
4.2 Experimental Result - Functional (2/4) -
Parachute release with dummy weight
Mission System Design > 4. Demonstration
Parachute release tests using dummy weight

## Slide 31
4.2 Experimental Result - Functional (3/4) - LEDs and Sound
Mission System Design > 4. Demonstration
Descriptions + pictures with annotations
  LEDs test for brightness / Sound Test

## Slide 32
4.2 Experimental Result - Functional
Mission System Design > 4. Demonstration
Descriptions + pictures with annotations
  GS protocol functionality using terminals
Satellite Terminal
GS Node Terminal

## Slide 33
4.2 Experimental Result - End-to-end testing (1/3) - CO2 sensor
Mission System Design > 4. Demonstration
CO2 GS Node
Measuring CO2 levels on the ground station
CO2 Measured results at GS

## Slide 34
4.2 Experimental Result - End-to-end testing (1/3) - CO2 sensor
Mission System Design > 4. Demonstration

## Slide 35
4.2 Experimental Result - End-to-end testing (2/3) - LEDs for landing
Mission System Design > 4. Demonstration

## Slide 36
4.2 Experimental Result - End-to-end testing - (3/3) - System
Mission System Design > 4. Demonstration
Full GS communications - Sat and CO2 node (using terminals)
Communications range test

## Slide 37
4.2 Experimental Result - End-to-end testing - (3/3) - System
Mission System Design > 4. Demonstration
Full GS communications - Sat and CO2 node (using terminals)
Communications range test
  While monitoring power
  and temperature

## Slide 38
4.2 Experimental Result - End-to-end testing - (3/3) - System
Mission System Design > 4. Demonstration
Reliability testing on software = > 1hr continuous satellite-GS operation

## Slide 39
4.3 Summary of Success Evaluation
Mission System Design > 4. Demonstration
Success Level | Goal No. | Mission Success Criteria | Verification Method | Result
Minimum Success | 1 | Establish the communication between Stellite and GS | Switch on the satellite and House Keeping Data Received | Success
 | 2 | Get the CO2 data from Satellite | CO2 data from Satellite is Received Successfully | Partial
 | 3 |  |  | 
Full Success | 4 | Establish the communication between Stellite and GS | Switch on the satellite and House Keeping Data Received multiple | Success
 | 5 | Get the CO2 data from Satellite at the specified interval of time to GS | CO2 data from Satellite is Received Successfully | Fail
 | 6 | Detect landing condition | LED and Sound data received | Partial
Advanced Success | 7 | Establish the communication between Stellite and different GS | Switch on the satellite and House Keeping Data Received continuous | Success
 | 8 | Get the CO2 data from Satellite at the specified interval of time from Different GS and Compare the results | CO2 data from Satellite is Received to all the GS station Successfully | Partial
 | 9 | Detect landing condition and measure the force of impact of the ground (through acceleration) | LED and sound data is received | Fail

## Slide 40
5. Conclusion
Was schedule planning appropriate? – Yes, but unforeseen challenges caused
the overall schedule not to be met
Was resource planning appropriate? – Yes.
Were risk identification and – Mostly, software development time was
countermeasures appropriate? not identified as a significant risk.
Was team communication appropriate? – Yes.
What was accomplished? – Full payload integration and test cycle
was experienced.
– One complete CO2 node and one partial onboard CO2 sensor.
– Fully functional bus and communication including payload data
What was learned? – Documentation takes time
– Software development can take more
time than expected
What is future work? – Improve GS software framework
– Better quality CO2 sensor
– Improved parachute to do complete drop test
Mission System Design > 5. Conclusion